## Slide 1
Sensing, Switching, Protection

## Slide 2
Solid-State and SPST Outputs
SPDT Outputs
84145
001-005
84145
010-015
84145
020-025
84145031
84145
041-046
84145
061-066
84145071
Compact 6.2mm Wide Package
N.O., SPDT, Transistor, or Triac Output
0.5A to 6A Outputs up to 250Vac
5Vdc to 230Vac/Vdc Inputs
LED Status Indicator
cURus Recognized, CE Compliant

## Slide 3
Protection of the control system is critical in nearly all applications. Faults occurring in a simple loop can be broken down as follows:
Sensor
25%
10%
Control
Actuator
40%
10%
15%
This indicates that 65% of all faults in a simple loop are caused by the sensors and actuators, and another 20% by the connections between them. The “control” part, which often comprises expensive components, such as PLC’s, controllers, electronic cards, etc., must be protected.
Simplified Control System Diagram and Typical Failure Percentage

## Slide 4
The interface modules also set the devices to the reference voltage. Simply put, this means that sensors and actuators can be connected to a control system with different input and/or output voltages.
The function of SIMM modules are to protect the control system from interference, over-voltage or short-circuits, which can occur with sensors connected to inputs or with actuators connected to outputs. The SIMM modules input and output are optically isolated, which provides galvanic isolation between the control system and the load.
Sensor
Control
OUT
IN
Actuator
(IPD, DPO, proximity sensors, etc.)
Output modules
Input modules

## Slide 5
In general, the current passing through control system input sensor is fairly low, as are the risks, compared with actuators, where the power required is greater. This explains why 95% of the modules sold are output modules. This interface function can be performed by many existing components on the market, such as SSR’s, electro-mechanical relays, I/O modules, interface terminals, etc., coming in numerous different sizes, shapes and types of fitting, etc.
The global interface component market has a turnover in excess of
5,400 million (USD), with a growth rate close to 5%. This growth can
be easily explained by the steady rise in the number of I/Os in control systems,
the increase in the power applied and the popular spread of small systems such as Millenium. It has also been noted that the trend is towards a reduction in the size
of these interface modules, as the size of control systems is on the decrease, and hence
that of cabinets too.

## Slide 6
    Phoenix Contact:
    Leading supplier in the specialist connection and interface market. Offers the largest range of interface modules (SIMM equivalent = PLC and DEK series). These are relay or solid state output modules with screw or spring connectors. But, they do not offer any controllers.
Crouzet strength: modules sold along with control systems.
Crouzet weakness: more limited range.
    Wieland:
    Connection specialist, but does not offer any control device. Its range includes only 1 or 2-relay output modules and 3 different casings for the same dimensions. These are the “FLARE” and “FLARE MOVE” product families (plug-in, interchangeable relay).
    Crouzet strength: modules sold along with control systems.
Crouzet weakness: none.
Competitive Summary

## Slide 7
Competitive Summary
    Finder:
    Relay manufacturer, which does not offer any solid state output module. All products come in a 6.2 mm format with a plug-in relay. There is the “38.8x series” for screw connectors and “38.9x series” for spring connectors. This range only includes 6 products in total.
    Crouzet strength: modules sold along with control systems.
    Crouzet weakness: no spring connector.
    Murr Elektronik:
    Connection and interface specialist, but offers almost no kind of control
    device. Extensive range, including a double (2-relay) module, but no
    spring connector. These products are in the MIRO range.
    Crouzet strength: modules sold along with control systems.
Crouzet weakness: more limited range.

## Slide 8
SSR's & Digital Input / Output Modules
Ronnie Haiduk (972) 471-2532 haidukr@us.crouzet.com
www.crouzet-usa.com/techtalk
Technical Resources

## Slide 9
Promotional Information
All Part Numbers Stocked
NED, IEN, ECN Press Release
Introduction Package
Stock Package (-10%)
Press Release
Catalog Pages
Product Samples